## Slide 1
CPOL Antenna and DTMF Control Capstone Senior Design Project March 17th, 2015
Tim Bodkin
Kevin Helms
Chris Tatosian
Luis Ceja Quiroz

## Slide 2: Problem Statement
Problem
  Degraded signal integrity of the UCSC repeater due to local terrain
Solution
  Improved reception by the addition of a circularly polarized antenna

## Slide 3: Project Requirements
Circularly polarized antenna array
DTMF controller
Antenna switching circuit
RoIP nodes
Audio linking Interface

## Slide 6: Antenna Switching Circuit
System that switches active antenna
Digital control and feedback signals

## Slide 7: Motivation
Real time switching between antennas
Switching event through DTMF tones

## Slide 8: Initial Design and Implementation
Power supply
Coaxial relays
Power MOSFETs
Two feedback signals

## Slide 9: Challenges
Rectified DC voltage higher than calculations predicted
Power resistors were found to get very hot
DTMF board can’t completely tell state of switching board

## Slide 10: Final Design
Added a fan to cool
Third feedback signal added

## Slide 11: Results
Reliable antenna switching

## Slide 12: DTMF Controller
Overview:
The DTMF Controller acts as a central control for the antenna switching system
  Logic is collected and sent between this circuit and the Linking Interface as well as the Switching Circuit
  Verifies DTMF sequences through hardware and switches between the VPOL and CPOL antenna upon an appropriate sequence

## Slide 13: Initial Design and Implementation
Initial Design included DTMF decoder chip MT8870 and an Atmega328P
  Atmega 328P provides enough GPIO ports for desired inputs, outputs, and additional pins for future work
  Atmega 328P inputs are compatible with Decoder outputs
Initial design involved Pulsed inputs using AND gates

## Slide 14: Challenges
Debugging
Slow Decoding
Pulsed signals had potential for timing errors, so instead designed to function with latched signals synchronous

## Slide 15: Results
Final Design
  Faster Decoding Time
  Latched Inputs
  LCD Display
  Status LED’s
  Manual Switch
  Audible Tone

## Slide 16: All Star Link Node
Overview
  Odroid U3
  Asterisk PBX
  AllStar Link
  Validated Users
  Security

## Slide 17: Approach and Initial Design
IRLP
Odroid U3
CM 108 Audio Codec
U3 I/O Daughter Board

## Slide 18: Challenges
Processing power
Software Installation
Device Driver
Little Documentation
No Support for Odroid
UDP Port Access

## Slide 19: Results

## Slide 20: Echolink Overview
      Open source VoIP system for amateur radio users
      Originally developed for windows, but later expanded to OS X and linux
      Over 200,000 validated users, about 5,000 online at any given time
      Security is based on callsign validation
      No known cases of malware or viruses from echolink (because it cant accept file data)

## Slide 21: Echolink: Approach
      Linux based single board computer (Raspberry Pi)
      Software used is SVX Link, an open source VoIP software package for amatuer radio
      Remote activation from field via DTMF commands
      Built in DTMF decoder

## Slide 22: Echolink: Initial Design
      Configured in Raspbian OS
      Configured static IP for SSH access on UCSC network
        User interface available by SSH
      Runs as a Daemon background process
      Control signals configured via GPIO pins on Raspberry Pi

## Slide 23: Echolink: Challenges
Controlling audio output so that both nodes can’t transmit at the same time
Cutsomization to fit our multi-node design

## Slide 24: Echolink: Final Design
Event based (GPIO) Python background script controls audio output to prevent both nodes transmitting at same time
Constantly running DTMF controller Echolink node

## Slide 25: Echolink: Results

## Slide 26: Linking Interface Overview
Central hub for all audio going between modules (DTMF controller, VoIP nodes) and the repeater

## Slide 27: Linking Interface: Approach
      Audio distribution amplifier for audio going to modules
      Audio summing amplifier for audio going to the repeater
      Embedded logic to prevent simultaneous audio transmission to repeater from VoIP nodes

## Slide 28: Linking Interface: Initial Design
      3.5mm mono audio jacks for audio connections
      Potentiometers (logrithmic, 10k) on audio channels going to repeater to allow for gain control on individual audio channels
      If one node is transmitting audio to repeater, other VoIP node is sent a ‘mute’ signal which is interpreted via a GPIO pin on each SBC, in the event that both nodes begin transmitting at the same time, Echolink is given priority
      Powered off of the same 12v supply that powers the repeater

## Slide 29: Linking Interface: Challenges
      Control logic on first 1st rev was over complicated and needed simplification
      Mistake with power supply pins on audio amplifier led to complications with testing
      The LM-2936 LDO didn’t give a steady 3.3v rail. Required additional capacitors to filter out high frequencies

## Slide 30: Linking Interface: Final Design
      Linking interface also provides power for the SBCs and DTMF controller
      Linking interface has DTMF controller stacked on top of it as daughter board
      Linking interface, DTMF controller, and SBCs are all within same casing

## Slide 31: Linking Interface: Results