## Slide 1
CPOL Antenna and DTMF Control Capstone Senior Design Project June 2nd, 2015
Tim Bodkin
Kevin Helms
Chris Tatosian
Luis Ceja Quiroz

## Slide 2: Amatuer Radio

## Slide 3: Repeaters

## Slide 4: Motivation
  Degraded signal integrity of the UCSC repeater due to local terrain
  Provide wider range of connectivity to the repeater and Amateur Radio community

## Slide 5: Solution
Circularly polarized antenna array
RoIP Nodes

## Slide 6: Approach
Modular System Design
Numerical EM Code Simulation
Augmentation of UCSC Repeater System
Permanent Installation

## Slide 7: System Overview
Circularly polarized antenna array
Antenna switching circuit
DTMF controller
RoIP nodes
Audio linking Interface

## Slide 8: System Overview

## Slide 9: System Overview

## Slide 10: Antenna Switching Circuit
System that switches active antenna
Digital control and feedback signals

## Slide 11: Motivation
Real time switching between antennas
Switching event through DTMF tones

## Slide 12: Initial Design and Implementation
Power supply
Coaxial relays
Power MOSFETs
Two feedback signals

## Slide 13: Challenges
Rectified DC voltage higher than calculations predicted
Power resistors were found to get very hot
DTMF board can’t completely tell state of switching board

## Slide 14: Final Design
Added a fan to cool
Third feedback signal added

## Slide 15: Results
Seemless antenna switching
Cool LEDs

## Slide 16: DTMF Controller
Overview:
The DTMF Controller acts as a central control for the antenna switching system
DECODES DTMF SEQUENCES
  Logic is collected and sent between this circuit and the Linking Interface as well as the Switching Circuit
  Verifies DTMF sequences through hardware and switches between the VPOL and CPOL antenna upon an appropriate sequence

## Slide 17: Initial Design and Implementation
Initial Design included DTMF decoder chip MT8870 and an Atmega328P
  Atmega 328P provides enough GPIO ports for desired inputs, outputs, and additional pins for future work
  Atmega 328P inputs are compatible with Decoder outputs
Software
Initial design involved Pulsed inputs using AND gates

## Slide 18: Challenges
Debugging
Slow Decoding/Decoder Timing
Pulsed signals had potential for timing errors, so instead designed to function with latched signals synchronous

## Slide 19: FD
Final Design
  Faster Decoding Time
  Latched Inputs
  LCD Display
  Status LED’s
  Manual Switch
  Audible Tone

## Slide 20: Echolink Overview
      Open source VoIP system for amateur radio users
      Originally developed for windows, but later expanded to OS X and linux
      Over 200,000 validated users, about 5,000 online at any given time
      Security is based on callsign validation
      No known cases of malware or viruses from echolink (because it cant accept file data)

## Slide 21: Echolink: Approach
      Linux based single board computer (Raspberry Pi)
      Software used is SVX Link, an open source VoIP software package for amatuer radio
      Remote activation from field via DTMF commands
      Built in DTMF decoder

## Slide 22: Echolink: Initial Design
      Configured in Raspbian OS
      Configured static IP for SSH access on UCSC network
        User interface available by SSH
      Runs as a Daemon background process
      Control signals configured via GPIO pins on Raspberry Pi

## Slide 23: Echolink: Challenges
Controlling audio output so that both nodes can’t transmit at the same time
Customization to fit our multi-node design

## Slide 24: Echolink: Final Design
Constantly running DTMF controller Echolink node

## Slide 25: Echolink: Results

## Slide 26: All Star Link Node
Overview
  What is All Star Link?
  Asterisk PBX
  Licensed and validated Radio Operators
  Security

## Slide 27: Approach and Initial Design
IRLP
  Closed source
  Required purchase of their products
Odroid U3
  DSP capabilities
CM 108 Audio Codec
U3 I/O Daughter Board

## Slide 28: Challenges
Processing power
Software Installation
Device Driver
Little Documentation
No Support for Odroid
UDP Port Access

## Slide 29: Linking Interface Overview
Central hub for all audio going between modules (DTMF controller, VoIP nodes) and the repeater

## Slide 30: Linking Interface: Approach
      Audio distribution amplifier for audio going to modules
      Audio summing amplifier for audio going to the repeater
      Embedded logic to prevent simultaneous audio transmission to repeater from VoIP nodes

## Slide 31: Linking Interface: Initial Design
      3.5mm mono audio jacks for audio connections
      Potentiometers (logrithmic, 10k) on audio channels going to repeater to allow for gain control on individual audio channels
      If one node is transmitting audio to repeater, other VoIP node is sent a ‘mute’ signal which is interpreted via a GPIO pin on each SBC, in the event that both nodes begin transmitting at the same time, Echolink is given priority
      Powered off of the same 12v supply that powers the repeater

## Slide 32: Linking Interface: Challenges
      Control logic on first 1st rev was over complicated and needed simplification
      The LM-2936 LDO didn’t give a steady 3.3v rail. Required additional capacitors to filter out high frequencies

## Slide 33: Linking Interface: Final Design
      Linking interface also provides power for the SBCs and DTMF controller
      Linking interface has DTMF controller stacked on top of it as daughter board
      Linking interface, DTMF controller, and SBCs are all within same casing

## Slide 35: Future Work
Final printed circuit board fabrication
Permanent system enclosures
Mount and test mutli-element antenna array

## Slide 36: Acknowledgements
Stephen Petersen (AC6Pete)
Jeff Bertalotto (KK6JGXXX)
Amateur Radio Community
Pornhub
Adderall
Vaping

## Slide 37: System Demonstration