## Slide 2: DTMF Controller
Overview:
The DTMF Controller acts as a central control for the antenna switching system
  Logic is collected and sent between this circuit and the Linking Interface as well as the Switching Circuit
  Verifies DTMF sequences through hardware and switches between the VPOL and CPOL antenna upon an appropriate sequence

## Slide 3: Initial Design and Implementation
Initial Design included DTMF decoder chip MT8870 and an Atmega328P
  Atmega 328P provides enough GPIO ports for desired inputs, outputs, and additional pins for future work
  Atmega 328P inputs are compatible with Decoder outputs
Initial design involved Pulsed inputs using AND gates

## Slide 4: Challenges
Debugging
Slow Decoding
Pulsed signals had potential for timing errors, so instead designed to function with latched signals synchronous

## Slide 5: Results
Final Design
  Faster Decoding Time
  Latched Inputs
  LCD Display
  Status LED’s
  Manual Switch
  Audible Tone

## Slide 6: All Star Link Node
Overview
  Odroid U3
  Asterisk PBX
  AllStar Link
  Validated Users
  Security

## Slide 7: Approach and Initial Design
IRLP
Odroid U3
CM 108 Audio Codec
U3 I/O Daughter Board

## Slide 8: Challenges
Processing power
Software Installation
Device Driver
Little Documentation
No Support for Odroid
UDP Port Access

## Slide 9: Results