## Slide 1: Echolink Overview
      Open source VoIP system for amateur radio users
      Originally developed for windows, but later expanded to OS X and linux
      Over 200,000 validated users, about 5,000 online at any given time
      Security is based on callsign validation
      No known cases of malware or viruses from echolink (because it cant accept file data)

## Slide 2: Echolink: Approach
      Linux based single board computer (Raspberry Pi)
      Software used is SVX Link, an open source VoIP software package for amatuer radio
      Remote activation from field via DTMF commands
      Built in DTMF decoder

## Slide 3: Echolink: Initial Design
      Configured in Raspbian OS
      Configured static IP for SSH access on UCSC network
        User interface available by SSH
      Runs as a Daemon background process
      Control signals configured via GPIO pins on Raspberry Pi

## Slide 4: Echolink: Challenges
Controlling audio output so that both nodes can’t transmit at the same time
Cutsomization to fit our multi-node design

## Slide 5: Echolink: Final Design
Event based (GPIO) Python background script controls audio output to prevent both nodes transmitting at same time
Constantly running DTMF controller Echolink node

## Slide 6: Echolink: Results

## Slide 7: Linking Interface Overview
Central hub for all audio going between modules (DTMF controller, VoIP nodes) and the repeater

## Slide 8: Linking Interface: Approach
      Audio distribution amplifier for audio going to modules
      Audio summing amplifier for audio going to the repeater
      Embedded logic to prevent simultaneous audio transmission to repeater from VoIP nodes

## Slide 9: Linking Interface: Initial Design
      3.5mm mono audio jacks for audio connections
      Potentiometers (logrithmic, 10k) on audio channels going to repeater to allow for gain control on individual audio channels
      If one node is transmitting audio to repeater, other VoIP node is sent a ‘mute’ signal which is interpreted via a GPIO pin on each SBC, in the event that both nodes begin transmitting at the same time, Echolink is given priority
      Powered off of the same 12v supply that powers the repeater

## Slide 10: Linking Interface: Challenges
      Control logic on first 1st rev was over complicated and needed simplification
      Mistake with power supply pins on audio amplifier led to complications with testing
      The LM-2936 LDO didn’t give a steady 3.3v rail. Required additional capacitors to filter out high frequencies

## Slide 11: Linking Interface: Final Design
      Linking interface also provides power for the SBCs and DTMF controller
      Linking interface has DTMF controller stacked on top of it as daughter board
      Linking interface, DTMF controller, and SBCs are all within same casing

## Slide 12: Linking Interface: Results